## Slide 1
Stage Tooling

## Slide 2
Our Specialty Since 1942!
Stage Tooling for Short to Medium Run Stamping:
  2,000 to 50,000 pieces annually
  Part Size: 0.5” x 0.5” to 24” x 36”
  All Metals – Steel, Stainless, Aluminum, Red and Yellow Alloys
  AS9100, ISO 901, ISO 14001, ITAR, Nadcap
Benefits Include:
  Low tooling cost, lower part price
  Available inventory of shared die sets reduce cost
  Shorter lead times & quick turnaround for product to market
  Rapid setup time with repeatable results for complex parts
  Accommodates quick part revision economically

## Slide 3
What is Stage Tooling?
  This method uses one tool for each stamping operation including: blanking, forming, piercing, contouring, etc.
  Shared common form die sets are used in production to lower the upfront cost.
  Tooling is built in-house and maintained by HV for the life of the part.
  Stage tooling offers low tooling costs and reduced part pricing from true fabrication method.

## Slide 4
Stage Tool Production
Stage 1:
Blanked
Stage 2:
Formed
Stage 3:
Pierced
  Example of a stamped part produced using separate Stage Tools.
  Typical stages include:
  Blanking
  Forming
  Piercing
  Contours
Click To Play Video

## Slide 5
Case Study – Window Mount Bracket

## Slide 6
Case Study – Process Comparison
Soft Tool Fabrication
  1) Laser
  2) Detab
  3) Sand
  4) Press brake hit 1 ▪ Set up ▪ Run – 4 hits
  5) Press brake hit 2 ▪ Set up ▪ Run – 2 hits
  6) Press brake hit 3 ▪ Set up ▪ Run – 1 hit
Progressive Die Stamping
  1) Progressive die ▪ Set up ▪ Run – 1 hit
Stage Tool Stamping
  1) Compound blank die ▪ Set up ▪ Run – 1 hit
  2) Wipe form die ▪ Set up ▪ Run – 1 hit
  3) Contour form die ▪ Set up ▪ Run – 1 hit
  4) V-form die ▪ Set up ▪ Run – 1 hit

## Slide 7
Case Study – Total Cost Analysis
  Stage Tool Break Even: ~2,750 pcs
  Progressive Die Break Even: ~21,000 pcs

## Slide 8
Case Study – Total Cost Analysis
  Stage Tool Break Even: ~2,750 pcs
  Progressive Die Break Even: ~21,000 pcs
Chart: Total Cost Analysis
| 1000 | 2500 | 5000 | 10000 | 25000 | 50000
Soft Tool | 6270 | 14030 | 26680 | 50680 | 121230 | 240980
Stage Tool | 11170 | 16955 | 21880 | 36780 | 80530 | 154780
Progressive Die | 40540 | 42725 | 46200 | 53250 | 74000 | 108250

## Slide 9
Stage Tooling Summary
2,000 – 50,000 pieces annually, most efficient process for low to medium volumes
Low upfront cost: $1,000s per tool
Lower piece price
In-house shared die sets reduce cost
Shorter tooling lead times
Quick turnaround for product to market (ROI)
Design freedom:
  Materials
  Easier to modify
  Complex geometries
  Tight tolerances
Short-run metal stamping offers a rapid setup time, minimal tooling investment, and repeatability for complex high-quality parts.

## Slide 10
Resource Links:
ISO 9001, AS9100 and ISO 14001 Certifications
Company Brochure
HV Team Directory
Sales Representative Directory
Customer TOC
Harvey Vogel Manufacturing Co.
sales@harveyvogel.com
harveyvogel.com
P: 651-739-7373